## Slide 1: A prototype of the next generation regional air-quality forecast system (Online-CMAQ)
Jianping Huang, Ivanka Stajner, Fanglin Yang, Raffaele Montuoro, Jeff McQueen, Ho-Chun Huang, Kai Wang, Hsin-Mu Lin, Chan-Hoo Jeon, Perry Shafran, etc.
A joint effort among NWS/EMC, OAR/ARL, CSL, GSD, USRA, UMBC, GMU, U. of Colorado, NDSU, and NESDIS/STAR
05/19/2022

## Slide 2: Outline
Motivation and objectives
UFS-based Online-CMAQ prototype
Preliminary testing and evaluations
Summary and an implementation plan
2

## Slide 3: Motivation and objectives
Status
  The GFS-driven CMAQ offline system provides 72-hr O3 and PM2.5 forecast for CONUS, AK, and HI twice a day at 06z and 12z cycles.
Motivation
  Wildfires, a major contributor to poor air quality have been increasing in the U.S. over the past several decades.
  Current operational model suffers from large uncertainties in wildfire emissions with respect to emissions intensity, speciation, duration, and diurnal evolution as well as smoke plume rise determination
  No any weather-air quality online coupling system has been tested from operational perspective at NOAA.
Objectives
  To build up the next-generation online regional air quality forecast system for the UFS AQ application
  To replace the operational air quality forecast system (GFS-CMAQ offline system) (to be implemented operationally in Q2 2023)
  To better represent the impact of chemistry on weather predictions as a member of the RRFS
3

## Slide 4
UFS
(Atmos)
NEXUS
CMAQ
(ML for Chem)
Anthrop.
Emission
Wild Fire
Emission
(RAVE)
POST
Bias Correction
Verification
(METPlus)
GFS
(ICs/BCs)
GEFS/Aero
+ GEOS/Chem
LBCs
Chem. Data Assimilation
Products
Web
Display
Satellite &
Surface obs.
A flowchart of the Online-CMAQ system
Machine Learning

## Slide 5: Online-CMAQ within the UFS framework
UFS-model
NOAA Air Quality Model (AQM)
Vertical Transport
Convection
Advection
Cloud and Radiation
NUOPC Layer
Read emissions (RAVE+ NEI)
IMPORT (includes grid)
EXPORT
AQM Infrastructure Layer
Chemistry
Aerosols
Column Chemistry
(CMAQ)
CMAQ: Community Multiscale Air Quality; NUOPC: National Unified Operational Prediction Capability
RAVE: Regional ABI and VIIRS fire Emissions; NEI: National Emission Inventory

## Slide 6: Features of the Online-CMAQ
Link the AQM with the UFS model dynamically
Using the same grids and physical schemes for meteorol. and chem. models
  Transport (horizontal and vertical) and mixing processes of chemical species are handled by the atmospheric model.
  Avoid the inconsistency between met and chem models (e.g., grid-mapping and loss of vertical levels) (model grids  write grids  AQ or CMAQ grids)
Two-way interactions between meteorological and chemical fields
  Feed the AQ model at each integration time step in stead of an hourly interval
  Provide the feedback to weather predictions (aerosol radiative feedback) (e.g., wildfires)
Heavy computational burden (challenge)
  Running time: increased by at least 8 times
  Variable number: 206 parameters in dyn files
  File size: large (20 GB dyn and 40 GB restart for the NA at a grid-spacing of 13 km)
6

## Slide 7
 | Oper (prod) (NAM-AQM) | v150_a (dev) (FV3GFS-AQM) | v161_a (UFS-AQM)
Met+CMAQ | NAM+CMAQv5.1.2 | GFSv15+CMAQv5.2 | UFS_Atmos+CMAQv5.2
Gas mechanism /Aerosol module | CB05 + Aero5 | CB06r3 + Aero6 | CB06r3 + Aero6
Grid_Spacing and vertical levels | 12 km / 35 levels | 13 km / 65 levels | 13 km / 65 levels
Anthropogenic Emi. | NEI 2016 | NEI 2016 (no plume rise) | NEI 2016 (no plume rise)
Fire Emission | HMS + BlueSky | RAVE (hourly, 0.03 deg.) | RAVE (hourly, 0.03 deg.)
Physics or CCPP suites | NAM (NMMB) | GFSv15_P2 | GFSv15_P2
Chem-LBCs | GEOS-Chem + NGACv2 | GEOS-Chem + GEFS/Aero | GEOS-Chem + GEFS/Aero
Model configurations for three simulations (or forecasts)

## Slide 8
O3

## Slide 9
A comparison of monthly mean daily 8-hr maximum surface O3 (MDA8) forecast bias (forecast – obs.) between the NAM-CMAQ (operational) and the Online-CMAQ forecast in August 2019.

## Slide 11
A comparison of monthly mean daily 8-hr maximum surface O3 (MDA8) forecast bias (forecast – obs.) between the NAM-CMAQ (operational) and the Online-CMAQ forecast in August 2019.

## Slide 12: Performance of O3
12

## Slide 13
Statistical evaluation of predited O3 over CONUS in August 2019
13

## Slide 14: Performance of PM2.5
14

## Slide 15
Statistical evaluation of predited CONUS PM2.5 over CONUS in August 2019
15

## Slide 16
WUS
EUS
Adjustment of eddy diffusivity improves nighttime over-prediction of O3 significantly. Kc = f(Ri)Kt , v143_b is same as v150_a

## Slide 17
PM2.5 fire emis.
PM2.5 FCST Bias
RAVE:

## Slide 18
CS: Operational AQM CONUS
AK: Operational Alaska
HI: Operational Hawai
G1: New RRFS domain at 3 km
G2: AQM_NA at 13 km
G2
G1
CS
AK
HI

## Slide 19: Summary, on-going work, and an implementation plan
UFS-based Online-CMAQ prototype has been developed and tested over the CONUS domain.
The Online system performs better than the previous operational model (i.e., NAM-driven CMAQ), especially PM2.5 predictions.
More capabilities such as Data Assimilation, Bias Correction, and AI emulation for accelerated transport of atmos. tracers are under development and will be integrated into the system.
The system has been testing over an extended domain to cover CONUS, AK, and HI.
The system will be running in real-time from June 1st, code will be frozen on Dec. 1st 2022, be delivered on March 1st, and be implemented in June 2023.

## Slide 20
Backup